## Slide 1: Infection Prevention in Point of Care Testing

## Slide 2: Point of Care Testing (POCT)
Diagnostic testing at or near the site of patient care
Uses portable handheld devices
Glucose testing most common

## Slide 3: Infection Control Concerns
Shared POCT devices are a potential vehicle for transmission of blood-borne pathogens, such as Hepatitis B
Some outbreaks of Hepatitis B in healthcare settings tied to lapses in standard precautions when glucometers and lancing devices were used for multiple patients

## Slide 4: Evaluate Equipment
Review POCT equipment such as lancing devices and glucometers to determine if equipment is designed for:
  Single-use (disposable)
  Health care professional use, and intended for multiple use per the manufacturer
  Patient self-testing, intended for use by one patient
Equipment designed for patient self-testing should NOT be employed for facility POCT

## Slide 5: Hand Hygiene and Gloves: CDC
Wear gloves during blood glucose monitoring
Remove and discard gloves after every patient
Change gloves that have touched potentially blood-contaminated objects or fingerstick wounds before touching clean surfaces
Perform hand hygiene immediately after the removal of gloves and before touching other medical supplies intended for use on other persons

## Slide 6: Fingerstick / Lancing Devices
CDC: Single-use, auto-disabling disposable fingerstick devices prevent reuse
  For use in settings where assisted monitoring of blood glucose is performed
  Discard entire device after one and only one use
CDC: Multiple use-capable lancing devices:
  Should ONLY be used by INDIVIDUAL persons for self-monitoring, not for assisted monitoring

## Slide 7: Glucometer
Shared glucometer is a potential vehicle for blood borne pathogen transmission
Whenever possible, glucometers should NOT be shared
CDC: If a glucometer must be shared, the device MUST be cleaned and disinfected after every use per the manufacturer’s instructions.
CDC: If the manufacturer does not specify how the device should be cleaned and disinfected, then it should NOT be shared.

## Slide 8: Insulin Pens
Risk of transmission of blood-borne pathogens from shared use
CDC: insulin pens are for single-patient use only and should NEVER be used for more than one person
Even if needles are changed between patients, contamination of the pen reservoir could result in transmission of blood-borne pathogens from a previous user

## Slide 9
Thank you